## Slide 1: Verilog 2001

## Slide 2: Combined port and data type
// Verilog-95
module adder (sum, co, a, b, ci) ;
output [31:0] sum;
output co;
input [31:0] a, b;
input ci;
reg [31:0] sum;
reg co;
wire [31:0] a, b;
// Verilog-2001
module adder (sum, co, a, b, ci) ;
output reg [31:0] sum;
output reg co;
input wire [31:0] a, b;
input wire ci;
// Verilog-2001
module adder (sum, co, a, b, ci) ;
output reg [31:0] sum;
output reg co;
input [31:0] a, b;
input ci;

## Slide 3: ANSI C style module declaration
// Verilog-95
module adder (sum, co, a, b, ci) ;
output [31:0] sum;
output co;
input [31:0] a, b;
input ci;
reg [31:0] sum;
reg co;
// Verilog-2001
module adder
(output reg [31:0] sum,
output reg co,
input wire [31:0] a,
input wire [31:0] b,
input wire ci );
// Verilog-2001
module adder
(output reg [31:0] sum,
output reg co,
input [31:0] a, b,
input ci );

## Slide 4: Module port parameter lists
// Verilog-95
module adder (sum, co, a, b, ci) ;
parameter MSB = 31,
LSB = 0;
output [MSB:LSB] sum;
output co;
input [MSB:LSB] a, b;
input ci;
reg [MSB:LSB] sum;
reg co;
wire [MSB:LSB] a, b;
// Verilog-2001
module adder
#(parameter MSB = 31, LSB=0)
(output reg [MSB:LSB] sum;
output reg co;
input wire [MSB:LSB] a, b;
input wire ci);

## Slide 5: Explicit in-line parameter Redefinition
// Verilog-95
ram mem1 ( … );
Defparam mem1.SIZE = 4096;
Defparam mem1.WIDTH = 12;
// Verilog-2001
ram mem1 #(.SIZE(4096), .WIDTH(12)) ( …);
// Verilog-95
ram mem1 #(12, 4096) ( … );
module ram (…);
parameter WIDTH =10;
parameter SIZE = 1024;
input [WIDTH-1:0] address_bus;
reg [WIDTH-1:0] core [0:SIZE-1:0];

## Slide 6: Fixed local parameter
// Verilog-95
parameter state1 = 4’b0001,
state2 = 4’b0010,
state3 = 4’b0100,
state4 = 4’10000 ;
// Verilog-2001
localparam state1 = 4’b0001,
state2 = 4’b0010,
state3 = 4’b0100,
state4 = 4’10000 ;
parameter | localparam
Can be declared in a module, task, or function | Can be declared in a module, task, or function
Can be redefined using defparam or in-line parameter redefinition | Cannot be redefined

## Slide 7: Comma Separated sensitivity lists
// Verilog-95
always @(a or b or ci)
sum = a + b + ci;
always @(posedge clk or negedge rst)
if (!rst)
q <= 0;
else
q <= d;
// Verilog-2001
always @(a, b, ci)
sum = a + b + ci;
always @(posedge clk, negedge rst)
if (!rst)
q <= 0;
else
q <= d;

## Slide 8: Combinational logic sensitivity lists
// Verilog-95
always @(a or b or ci)
sum = a + b + ci;
// Verilog-2001
always @(*)
sum = a + b + ci;
// Verilog-2001
always @*
sum = a + b + ci;

## Slide 9: Disabling implicit net declaration
Verilog-95
  Automatically infer net data type where
    When a signal name appears in the connections to an instance of module or primitive
    When a signal name is on the left side of a continuous assignment (and not declared)
// Verilog-95
module bad_chip (o1, n0, n1);
output o1;
input n0, n1;
and (o1, no, nl) ; // two typos ->
// the misspelled names simply
//infer a new list
endmodule
// Verilog-2001
`default_nettype none
module bad_chip (o1, n0, n1);
output o1;
input n0, n1;
and (o1, no, nl) ; // two typos ->
// undeclared signal names ->
// compile errors
endmodule