## Slide 1: Synchronous Design Labs
Kang Yi
HGU

## Slide 2: Traffic Light Controller Example
highway farmway
S0 Green Red
S1 Yellow Red
S2 Red Green
S3 Red Yellow
highway
farmway
Traffic_light
controller
clk
rst
X
hwy
fwy
x
x
X : sensor that indicates
if there is a traffic in the farmway
Output Table (Moore type)
S0
S2
S1
S3
X=0
X=1
X=1
X=0
start

## Slide 3: Traffic Light Controller Verilog Source
// traffic light definition
`define YELLOW 2’d0
`define RED 2’d1
`define GREEN 2’d2
// state assignment definition
`define S0 2’b00
`define S1 2’b01
`define S2 2’b10
`define S3 2’b11
module sig_controller
(hwy,fwy, X, clk,rst) ;
output [1:0] hwy, fwy;
reg [1:0] hwy, fwy ;
input X, clk, rst ;
reg [1:0] cs, nst ; // state variable
always @(posedge clk or posedge rst)
if(rst) cs <= `S0;
else cs <= nst;
always @(cs or x) case (cs)
`S0 : if(X) nst = `S1; else nst = `S0;
`S1 : nst = `S2;
`S2 : if(X) nst = `S2; else nst = `S3;
`S3 : nst = `S0;
endcase
always @(cs)
case (cs)
`S0 : begin hwy = `GREEN; fwy = `RED; end
`S1 : begin hwy = `YELLOW; fwy = `RED; end
`S2 : begin hwy = `RED; fwy = `GREEN; end
`S3 : begin hwy = `RED; fwy = `YELLOW; end
endcase
endmodule
Next state
FSM Output

## Slide 4: Testbench
module testbench;
reg clk = 0;
reg rst ,X ;
wire [1:0] hwy, fwy;
module sig_controller (hwy,fwy, X, clk,rst) ;
initial forever #5 clk = ~ clk; // or always #５ clk = ~ clk;
initial begin
rst = 1;
#10 rst = 0; X = 1;
#40 X = 0;
#20 X = 1;
#10 rst = 1;
#10 rst = 0;
#20 $stop;
end
endmodule

## Slide 5: TLC Lab Block Diagram
TLC FSM
clock enable generator
100Hz
0.5Hz
Color_LED
Driver
Debounce
&pulse_gen
Color_LED
Driver
en
en
100MHzClk
hwy
fwy
BTN
X
R1 G1 B1
R2 G2 B2
Yellow=R+G
Red=R
Green=G

## Slide 6: Making FSM Slow-down by using clock enable for state register update control
Compute
Next state
(조합회로)
State
register
Compute
output
(조합회로)
input
output
Current state
Next
state
100MHzClk
enable
ce
D
Q
rst

## Slide 7: Exercises
Design a Dice Game Machine. The game is played with 2 dices. The controller inputs are X, clock, and reset. The outputs are Win, Lose, Dice0[2:0], and Dice1[1:0]. The Flowchart for the game is as follows.
Sum = 6
Point <= sum
Roll two dices
Sum = 7 or 11
Yes
No
Yes
No
Roll two dices
Sum = 7 or 6
Sum = Point
lose
win
win
lose
Yes
Yes
No

## Slide 8: Hints for the Ans (1)
win
lose
clk
Reset
roll
Dice game
win
lose
controller
D6
D7
D11
ld
inc
reset roll
clock
eq
datapath
The Top-Level Submodules
Synchronizer
roll

## Slide 9: Hints for the Ans (2)
The Datapath and Control Signals
Game
controller
D7
D11
D6
eq
roll
loadP
Inc1
win
lose
Dice0
Dice1
3-bit Adder
Decoder
D7
D11
D6
Point Reg
comparator
eq
loadP
inc1
inc2
Dice Game Datapath
clk

## Slide 10: Hints for the Ans (3)
S0
S4
S2/win
S3/lose
S1
S5
roll’ rq’(D7 +D6)
roll/inc
roll’ Eq’D7’ D6’
roll’
roll’ D7’ D11’ D6’/ld
roll/inc
roll’ eq
roll
reset’
reset’
roll’ D6
roll’ (D7+D11)
roll
S0 is an initial state
This FSM has Synchronous Reset
reset
reset
roll’
The Game Controller

## Slide 11: Hints (Synchronizer Design)
System
core logic
Sometimes Asynchronous Inputs are unavoidable (e.g. User Inputs: roll)
Asynchronous Inputs : Signals from different Clock Domain
Synchronizer Objectives : Synchronization & DeBouncing
Clock A
A
Y
Asynchronous
Inputs X
Clock domain A
Clock domain B
Clock B
X
A
Y
Clock A

## Slide 12: Dice Game Lab Extension
Add Dice0, Dice1, Point, and Sum value output port to the datapath
Add 7segment display to the game top module
Add state indicator with LEDs (Win, Lose, Wait)
datapath
Dice0
Dice1
Point
Sum
controller
7 segment display driver
status
a b ,… ,g
AN3 AN2 AN1 AN0
state
decoder
Win Lose Wait Init
roll
sync

## Slide 13: Candy Vending Machine
50원, 100원 동전 사용 가능
Candy값: 150원,
200원 이상 입력시 잔돈 배출
시작
sum  0
50원 입력?
100원 입력?
sum  sum+50
sum  sum+100
sum >= 150
sum == 200
LED1
N
N
Y
Y
LED2
Y
Y
N
N

## Slide 14: Datapath
sum
0 1
0 1
50 100
0
sel2
sel1
+
dec
GE150
EQ200
ld
LED1
LED2
LED2_clr
LED2_set
LED1_set
LED1_clr
D Q
D Q
Q_in
LED1: 물건출력
LED2: 잔돈출력
GE150: sum>=150
EQ200: sum=200
ld: load sum reg
sel1, sel2 : MUX sel

## Slide 15: Controller
S0/
sum0
S1
S2
/sum  sum+50
S3/
sum sum+100
EQ200
100원
50원
S4
S5/
sum 0, LED1set
S6/
LED2set
GE150
start
S0
start
sm 0
S1
S2
100원/
sum
sum+100
50원/
sum
sum+50
GE150, GE200’/
LED1_set
GE150, GE200/
LED1_set,
LED2_set
GE150’, GE200/-
No input
No input
LED1clr, LED2clr 신호는?

## Slide 16: n-bit Add & Shift Multiplier Lab (v1)
Product(A)  Multiplicand(B) * Multiplier(Q)
x
Multiplicand (B=9) 1001
Multiplier(Q=11) x 1011
---------
1001
1001
0000
1001
---------
Product(A:99) 1100011
Q(multiplier): 1011
B(multiplicand): 1001
A(Product): 0000

## Slide 17: n-bit Add & Shift Multiplier Lab (v2)
{N, Q}
 A * B
datapath

## Slide 18: Multiplier Extension Lab
Multiplier
start
done
main_ctrl
8
Product
(A,Q)
7segment display
B
A
Reg Y
Reg X
CA ~ CG
AN[7]~ AN[0]
SW7~SW4
SW3~SW0
cvBCD4
BTN
4
4
bin2BCD255
cvBCD4
0
sync
bin2BCD_start
Ld_in
go
multiply
stop